## Slide 1
AMRUPT (Animal Movement Research Using Phase-based Trilateration)

## Slide 2
This week
“Engineering design process”
AMRUPT project consultation
Obtain pertinent information for generating a proposal for this semester’s work.
Generate list of questions to help you define the problem, and to gather background information

## Slide 3
Step 1: Begin planning for the design process
Khandani, 2005

## Slide 4
Step 1: Begin planning for the design process
Khandani, 2005

## Slide 5
Define the problem
1. Identify and establish the need
“A common tendency is to begin generating a solution to an apparent problem without understanding the problem.”
2. Develop a problem statement
“To reach a clear definition, [engineers] collect data, run experiments, and perform computations that allow a need to be expressed as part of an engineering problem-solving process.”
3. Establish explicit criteria for success
The design must collect accurate data.
The design must collect sufficiently precise data.
The design must be fast.
The design must be low cost.
The design should be safe.
The design should be simple to operate, with minimum human effort.

## Slide 6
Requirements and constraints
Short range: 150m min, 300 m ideal, between receivers
Extremely simple transmitter design: lightweight (150 mg ideal, 300 mg upper limit), low power
Data sample rate: <5s interval ideal, 10s upper limit
Datalogging / data management: each receiver must receive data from ~20-50 tags at 5s interval each for 1 day, data must be uploaded to central hub automatically, physical retrieval from hub can occur daily , triangulation need not occur before data is retrieved, can use cellular networks
Duration of datalogging: system should remain operational 3-4 months
GUI: not needed for visualizing bird locations, but need a way to identify system operation status either from the hub or from each ground-node
System can operate in cluttered environments: multipath interference
Number of mobile nodes: 50 adequate, upper limit of 1000 for total # deployed; expect only 0-20 mobile-nodes to be within range of a given ground-node at a time
High spatial accuracy for triangulation results: ~5 m
Low cost receivers: COTS components
Low power consumption of receivers: can operate on solar power
2D localization (lat,long) OK, 3D (lat,long,azimuth) ideal
Communication protocol: Time division multiplexing (not frequency) to maximize Tx sleep modes
Forward compatibility: Must be compatible with and adaptable to a multi-frequency-phase-integer-disambiguation approach for future versions

## Slide 7
Engineering design process
Khandani, 2005

## Slide 8
Gather pertinent information
1. Refine your thinking about the problem, and place it in context
Is the problem real and its statement accurate?
Is there really a need for a new solution or has the problem already been solved?
What are the existing solutions to the problem?
What is wrong with the way the problem is currently being solved?
What is right about the way the problem is currently being solved?
2. Search for information sources
Scientific encyclopedias and technical handbooks.
Primary articles
Faculty in ECE and beyond
Company websites and brochures

## Slide 9
Gather pertinent information

## Slide 10
Engineering design process
Khandani, 2005

## Slide 11
Generate multiple solutions
Synthesize ideas from existing work
“Start with existing solutions to the problem and then tear them apart to find out what's wrong with those solutions and focus on how to improve their weaknesses.”
Brainstorming important!!
“Ideas are generated when people are free to take risks and make mistakes.”
“Brainstorming at this stage is often a team effort in which people from different disciplines are involved in generating multiple solutions to the problem.”

## Slide 12
3 tiered approaches (phases)
Obtain Phase-difference information, AOA
Schedule Tx/Rx
Tx from mobile-node
Rx from ground-node
Obtain ID and timestamp
Transmit AOA, ID, timestamp to base station
Triangulate location
Phase I (single frequency)

## Slide 13
3 tiered approaches (phases)
Obtain Phase-difference information, AOA
Schedule Tx/Rx
Tx from mobile-node
Rx from ground-node
Obtain ID and timestamp
Transmit AOA, ID, timestamp to base station
Triangulate location
Phase II (multi-frequency)
MF Tx from mobile-node
Obtain MF Phase-difference information
Refine phase-difference estimates, AOA
Location estimate insufficiently accurate?

## Slide 14
3 tiered approaches (phases)
Obtain Phase-difference information
Schedule Tx/Rx
Tx from mobile-node
Rx from ground-node
Obtain ID and timestamp
Transmit AOA, ID, timestamp to base station
Triangulate location
Phase III (multi-frequency phase integer disambiguation)
MF Tx from mobile-node
Obtain MF Phase-difference information
Refine phase-difference estimates, AOA
Disambiguate phase integer
Trilaterate location w/ ranging
Location estimate insufficiently accurate?
Transmit phase int, ID, timestamp to base station

## Slide 15
Watson-Watt pair 1
Watson-Watt pair 2
Antenna 2
Antenna 3
Antenna 4
DF Algorithm running on RaspberryPi
Antenna 1
LNA
LNA
LNA
LNA
Demodulator
&
IF Mixer
Local Oscillator
ADC
I
Q
1
2
3
4
1
2
3
4
CC1310
I/Q
RF in
ID out
Trigger
signal
control
Option 1
Notes: TDOA

## Slide 16
Watson-Watt pair 1
Watson-Watt pair 2
Antenna 2
Antenna 3
Antenna 4
DF Algorithm running on RaspberryPi
Antenna 1
I/Q 1
I/Q 3
I/Q 4
RF Switch
CC1310
I/Q 2
I/Q 1-4,
RSSI 1-4, ID
AOA,
RSSI,
ID,
Time
LNA
LNA
LNA
LNA
Local Oscillator
Option 2
SPI
signal
control
Notes: TDOA

## Slide 17
Watson-Watt pair 1
Watson-Watt pair 2
Antenna 2
Antenna 3
Antenna 4
DF Algorithm running on RaspberryPi
Antenna 1
I/Q 1, RSSI 1, ID
I/Q 3,
RSSI 3
I/Q 4,
RSSI 4
CC1310
I/Q 2,
RSSI 2
AOA,
RSSI,
ID,
Time
LNA
LNA
LNA
LNA
Local Oscillator
Option 3
signal
control
CC1310
CC1310
CC1310
RF switch
LFM signal
Notes: TDOA

## Slide 18
TRX 1
TRX 2
TRX3
TRX4
GPS
Compass
Time-keeping,
coordination w/txrs
coordination w/ rxrs
localization of receivers
Orienting antenna elements
Energy harvesting
Automated phase-based telemetry receiver system
RxTx communication protocol
Antenna 2
Antenna 3
Antenna 4
Local
Oscillator
DF Algorithm running on RaspberryPi
CC1310 1
Low Noise
Amplifier
Low Noise
Amplifier
Low Noise
Amplifier
Antenna 1
Low Noise
Amplifier
CC1310 2
CC1310 3
CC1310 4
Antenna 2
Antenna 3
Antenna 4
Local
Oscillator
DF Algorithm running on RaspberryPi
CC1310 1
Low Noise
Amplifier
Low Noise
Amplifier
Low Noise
Amplifier
Antenna 1
Low Noise
Amplifier
CC1310 2
CC1310 3
CC1310 4
Antenna 2
Antenna 3
Antenna 4
Local
Oscillator
DF Algorithm running on RaspberryPi
CC1310 1
Low Noise
Amplifier
Low Noise
Amplifier
Low Noise
Amplifier
Antenna 1
Low Noise
Amplifier
CC1310 2
CC1310 3
CC1310 4
Antenna 2
Antenna 3
Antenna 4
Local
Oscillator
DF Algorithm running on RaspberryPi
CC1310 1
Low Noise
Amplifier
Low Noise
Amplifier
Low Noise
Amplifier
Antenna 1
Low Noise
Amplifier
CC1310 2
CC1310 3
CC1310 4

## Slide 19
5 + X s
Ground node
(acquire or sleep mode)
5 min – (5 + X s)
Tx
Rx from mobile nodes
5 s
Tx countdown signal (5 s)
e.g. timestamp & checksum
e.g. timestamp & checksum
0.0000
X (?) s
Tx commands
Checksum (opt.)
Global time
Sleep command
Sleep length
Y
N
X
Default?
Y
N
Listen for tags
Special commands for Y tags
X
Y IDs
*Keeps all mobile nodes from TXing when system isn’t monitoring
*Default mode just has any tag within range of sync signal transmit at its scheduled time
Y commands
*Special commands allow a subset of tags to be told to go to sleep, switch to different mode (e.g. to upload sensor data on different channel), etc.
*All mobile nodes sync’d here
X
*Give mobile nodes way to check that they have a good link
*Will need a data upload mode too
Mobile-to-Ground Node Communication Protocol
Notes: Mobile node diagram to follow. Mobile nodes should sleep just under 5 s (ensuring they will hear a ground node transmission at least once if it is in range), then wake long enough to receive a single countdown signal from a ground node. Once they have received a countdown signal, and the checksum demonstrates a good link, update global time (it will have drifted over the last 5 min), then listen for rest of commands. Once commands received use global time, received command, and (assuming the command includes a simple transmit instruction) pre-programmed transmission time delay to send ID during the ground node’s ~5 min RX period.

## Slide 20
TRX 1
TRX 2
TRX3
TRX4
GPS
Compass
Trilateration algorithm
Uses RSSI?
Machine learning w/ calibration beacons?
Time-keeping,
coordination w/txrs
coordination w/ rxrs
localization of receivers
Orienting antenna elements
Energy harvesting
Automated phase-based telemetry receiver system
RxTx communication protocol
Bluetooth / VHF uplink to central hub
Node-to-node VHF uplink
Antenna 2
Antenna 3
Antenna 4
Local
Oscillator
DF Algorithm running on RaspberryPi
CC1310 1
Low Noise
Amplifier
Low Noise
Amplifier
Low Noise
Amplifier
Antenna 1
Low Noise
Amplifier
CC1310 2
CC1310 3
CC1310 4
Antenna 2
Antenna 3
Antenna 4
Local
Oscillator
DF Algorithm running on RaspberryPi
CC1310 1
Low Noise
Amplifier
Low Noise
Amplifier
Low Noise
Amplifier
Antenna 1
Low Noise
Amplifier
CC1310 2
CC1310 3
CC1310 4
Antenna 2
Antenna 3
Antenna 4
Local
Oscillator
DF Algorithm running on RaspberryPi
CC1310 1
Low Noise
Amplifier
Low Noise
Amplifier
Low Noise
Amplifier
Antenna 1
Low Noise
Amplifier
CC1310 2
CC1310 3
CC1310 4
Antenna 2
Antenna 3
Antenna 4
Local
Oscillator
DF Algorithm running on RaspberryPi
CC1310 1
Low Noise
Amplifier
Low Noise
Amplifier
Low Noise
Amplifier
Antenna 1
Low Noise
Amplifier
CC1310 2
CC1310 3
CC1310 4

## Slide 21
Engineering design process
Khandani, 2005

## Slide 22
Analyze and select a solution
1. Systematic analysis of design solutions
Functional analysis – will it function the way it should?
Mechanical/Strength analysis – is it physically durable?
Manufacturability/Testability – can it be produced easily? Is it overly complex?
Product safety and liability – will it be safe for the user?
Economic and market analysis – is it affordable / cost-effective?
Regulatory and Compliance – is it legal (think about FCC regulations)?
2. The decision process: how to choose among the options?
Think about using a decision matrix:
  Functionality: 30 %
  Cost: 20 %
  Complexity: 20 %
  Safety: 20 %
  Use of standard parts: 10 %
A | B | C
25 | 30 | 15
20 | 15 | 20
10 | 20 | 20
20 | 20 | 20
5 | 10 | 5
A | B | C
25 | 30 | 15
20 | 15 | 20
10 | 20 | 20
20 | 20 | 20
5 | 10 | 5
80 | 95 | 80

## Slide 23
Engineering design process
Khandani, 2005

## Slide 24
Test and implement the solution
1. Prototyping
Simulations and simplified models to evaluate if you’re on the right track. Help define what other considerations may be need to be met before getting too far.
2. Documentation (!!!!)
“One of the most important activities in design is documenting your work, clearly communicating the solution to your design problem so someone else can understand what you have created.”

## Slide 25
In-line comments
“ReadMe”file
Good documentation is essential!

## Slide 26
Test and implement the solution
1. Prototyping
Simulations and simplified models to evaluate if you’re on the right track. Help define what other considerations may be need to be met before getting too far.
2. Documentation (!!!!)
“One of the most important activities in design is documenting your work, clearly communicating the solution to your design problem so someone else can understand what you have created.”
3. Testing and verification
Without proper testing at all stages in the process, you may find yourself making costly mistakes later.
Standardized test sets to evaluate functionality across semesters

## Slide 27
Engineering design process
Khandani, 2005
Project Proposal
Define the AMRUPT Problem